## Slide 1
Smart Plant Monitoring System
Instructor: Prof. Arpit Khandelwal
Team Members:
Jyotiraditya Singh Rathore B23ES1017
Shreyansh Agarwal B23PH1024
ES and IoT

## Slide 2
  Water Efficiency & Sustainability: Automate irrigation to reduce water wastage by watering only when soil moisture is low.
  Low-Cost Smart Agriculture: Provide an affordable, IoT-based solution using ESP8266 and basic sensors for small-scale farmers or gardeners.
  Real-Time Remote Monitoring: Enable users to monitor and control plant health from anywhere via MQTT promoting convenience and scalability.
  Power-Efficient IoT Design: Implements event-based data publishing and periodic sensor polling to minimize energy consumption, ideal for low-power IoT environments.
MOTIVATION

## Slide 3
i.Title: Smart Plant Monitoring System
ii. Objective:To automate plant health monitoring
and using low-cost IoT components and enable remote control
and alerts via MQTT.
iii. Key Features:
  Soil moisture sensing with automatic and manual motor control
  Temperature and humidity monitoring via DHT11
  Nutrient (NPK) measurement using Modbus communication
  Motion detection using PIR sensors
  Real-time data publishing and alerts using MQTT
iv. Target Users:Home gardeners, small-scale farmers,agricultural researchers,
and IoT learners.
v. Technologies Used: Hardware: ESP8266 NodeMCU, DHT11, Moisture sensors, PIR sensors, NPK sensor,
Motors, MQTT protocol, PubSubClient, ModbusMaster library.
PROJECT OVERVIEW

## Slide 4
Initialization:
  ESP8266 connects to Wi-Fi.
  MQTT client connects to the MQTT broker.
  Sensors (moisture, PIR, temperature, humidity, NPK) are read, and initial data is published.
Sensor Data Collection:
  Periodic readings from moisture sensors, PIR sensors, DHT11, and NPK sensor.
  Moisture levels are compared to thresholds to decide if watering is needed.
Motor Control:
  If moisture is below threshold, motor starts watering the plant.
  If moisture is above threshold, motor stops watering.
  Manual motor control via MQTT commands.
Data Publishing:
  Sensor data (moisture, PIR, temperature, humidity, NPK) is published to MQTT topics.
  Only updated values are sent to reduce traffic and power consumption.
  Notifications:
    Notifications (e.g., watering started/stopped, motion detected) are sent to MQTT for monitoring.
  Wi-Fi/MQTT Reconnection:
    Automatically reconnects if Wi-Fi or MQTT connection drops.
WORKFLOW

## Slide 5
ESP8266:
  Controls sensors and motors.
  Manages Wi-Fi and MQTT communication.
Wi-Fi Network:
  ESP8266 connects to a local Wi-Fi network to access the MQTT broker.
MQTT Broker:
  Acts as a central point for communication, receiving sensor data and sending
motor control commands.
Sensors:
  Moisture Sensors: For soil moisture measurement.
  PIR Sensors: For motion detection.
  Temperature and Humidity (DHT11): For environmental monitoring.
  NPK Sensor: For soil nutrition (using Modbus communication).
Motor Control:
  Motors are activated/deactivated based on soil moisture readings and user input
(via MQTT).
ARCHITECTURE

## Slide 6
  Successfully built a smart system that monitors soil moisture, temperature, humidity, NPK levels, and motion, triggering irrigation automatically when needed.
  Gained hands-on experience with ESP8266, sensor integration, and real-time data communication using MQTT.
  Understood the fundamentals of IoT-based automation, including sensor calibration, wireless communication, and embedded system design.
Results and Learning

## Slide 7
FUTURE SCOPE
  Integration of image processing and machine learning to detect plant diseases, nutrient deficiencies, or pest infestations using camera input.
  Use of NPK and moisture sensor data to automatically control nutrient injectors and irrigation systems for optimal plant growth (precision agriculture).
AI-Based Plant Health Diagnosis:
Automated Nutrient and Water Dosing:
Cloud Connectivity and Mobile App Integration:
  Real-time monitoring and control via a mobile app or web dashboard, with features like historical trends, plant care reminders, and push notifications for anomalies.

## Slide 8
Thank you